## Slide 1: Multicasting in Mobile Ad-Hoc Networks (MANET)
Project Supervisor: Michael Hitchins
Student Id: 41543491
RajKumar Sood

## Slide 2: Agenda
Introduction
Issues and Challenges in Multicasting for MANET
Classification of Multicasting Protocols
Simulation Based Comparison
Security Threats and Challenges in MANET
Conclusion

## Slide 3: What is Mobile Ad Hoc Network (MANET) ?
Definition
A system of Mobile nodes connected with each other via wireless medium without infrastructure support
Applications
  Military battlefield
  Emergency rescue
  Conferences
  Outdoor Internet access on campuses

## Slide 4: Why choose Mobile Ad Hoc Network ?
Pros
  Easy Deployment
Cost Effective
Time Effective
  Better reachability
  Wider accessibility
  Network of the Future
Cons
  Immature
  Flow and congestion problems
  Security issues
  Interoperability

## Slide 5: What is Multicasting ?
Definition
Multicasting is efficient mean of providing data from a single source to a group of receivers simultaneously
Benefits for MANETs
  Bandwidth Efficiency
  Lower network overhead
  Lower energy consumption
  Reduce communication cost

## Slide 6: Issues and Challenges
Dynamic multi hop topology
  Constant node movement
  Network Resource Usage Efficiency
    Scarce bandwidth availability
  Power Consumption
    Limited power supply in hand held devices
  Reliability and Security
    Transmission over wireless medium
  Quality of Service
    Reserve network resources to prevent jitter, packet loss
  Mobility
    leads to construction of trees and meshes that are not efficient leading to packet loss

## Slide 7: Classification of Multicasting Protocols
Proactive Multicast
Table Driven
Every node maintains up to date information
Pros
  Low Route acquisition latency
  Cons
    High Control Overhead
Reactive Multicast
On demand
Routes are created on demand
Pros
  Less Control Overhead
Cons
  High Route acquisition latency

## Slide 8: Classification of Multicasting Protocols
Tree Based Multicast
  Tree based Mechanism
  Single Path between the source and destination
  Uses JOIN TREE messages to construct a tree
  Source Tree Based
    Tree created by each source
    As many number of trees as source
    Shared Tree Based
      Single multicast tree for all sources
      Single tree includes all source nodes

## Slide 9: Multicast Tree

## Slide 10: Classification of Multicasting Protocols
Mesh Based Protocols
  Mesh based Mechanism
  Multiple paths between the source and destination
  Uses JOIN MESH and JOIN REQUEST messages for mesh construction
  Hybrid Protocols
  Combination of tree and mesh based protocols
  Multiple routing paths
  Create non optimal tress due to node mobility

## Slide 11: Multicast Mesh

## Slide 12: Multicast Ad Hoc On Demand Distance Vector Routing Protocol (MAODV)
On Demand tree based protocol
Discovers multicast route on demand
Involves different stages ,
  Multicast Route Discovery (RREQ messages)
  Reverse Path Setup (RREQ messages)
  Forward Path Setup (RREP messages)
  Multicast Route Activation (MACT messages)
  Group Hello Messages (GRPH messages)

## Slide 13: Different Stages
Multicast Route Discovery
Reverse path Setup
Forward Path Setup
Multicast Route Activation

## Slide 14: On Demand Multicast Routing Protocol (ODMRP)
On Demand Mesh Based Protocol
Uses the concept of ‘forwarding group’
Floods JOIN QUERY packets
JOIN REPLY packets establish multicast routes & forwarding members

## Slide 15: Different Stages for ODMRP
Mesh creation
Join Query Process
Join Reply Process

## Slide 16: Qualitative Comparison of MAODV and ODMRP

## Slide 17: Simulation Based Comparison
Simulation Parameters

## Slide 18: Simulation based Comparison
Network Parameters
  Number of Senders
  Multicast Group Size
  Mobility
  Metrics
    Packet Delivery Ratio
    Control Overhead
    Packet Transmission Ratio
    Control and Data packets delivered per Data Packet delivered

## Slide 19: Number Of Senders

## Slide 20: Mobility

## Slide 21: Multicast Group Size

## Slide 22: Protocol Analysis
ODMRP has a better packet delivery ratio than MAODV
ODMRP is more robust than MAODV due to minimal packet loss and availability of multiple routes
ODMRP is less scalable compared to MAODV as the number of senders or multicast group size is increased
MAODV has minimal control overhead as compared with ODMRP

## Slide 23: Security Threats and Challenges
Types of Attacks
  Routing Attacks
  Packet Filtering Attacks
  Challenges for Security
    Peer-to-peer Architecture
    Scarce Availability of resources
    Node mobility and wireless channels demand more Dynamics in MANET

## Slide 24: Conclusions
Multicasting plays a very important role in supporting a variety of applications characterized by close degree of collaboration for MANETS
Mesh based protocols outperform tree based protocols as they are more robust
Usefulness of different protocols depends on the application environment
Multicasting protocols for MANET are in early stages and need further research
Issues like QoS, reliability, security needs to be further investigated